## Slide 1
Policy and practice concerning the reduction of odour nuisances in the Netherlands
By Hugo van Belois
EC Seminar Poland,
Miedzyzdroje, 31 March 2008
OpdenKamp Environmental Consultancy

## Slide 2: Content
Introduction
Situation in the Netherlands
Our policy and practice in general
Industry : odour control in detail
Agriculture: its regulations and results
Conclusions and recommandations

## Slide 3: 1. Introduction
Speach prepared together with
Dutch Ministry of Environmental Protection
Own background in
    Odour measurements
    Policy on air pollution and odour (national/regional)
    Consultancy on odour control and surveys

## Slide 4: The Dutch Odour situation

## Slide 5: 2. Situation in the Netherlands
Over 25 years of policy development
Main sources of odour nuisance
    Agriculture 30%
    Households 30%
    Industry 25%
    Traffic 15%

## Slide 6: 2. Complaints on the Environment
70% – 80% ODOUR
Noise
Air
Soil
Water
Others

## Slide 7: Odour Nuisance in the Netherlands
Odour
Nuisance
Overall
1981 45%
30%
Severe
Nuisance
still
2 - 8%

## Slide 8: Regional differences NL
Regions with livestock farming
    Nuisance 15 – 40%
    Severe Nuisance 5 – 20%
Highly industrialised areas
    Nuisance 25 – 70%
    Severe Nuisance 10 – 40%
Quiet Regions
    Nuisance < 5 – 10 %
    Hot Spots around specific sites (landfills etc)

## Slide 9: 3. Dutch Legislation on Odour
Spatial Planning Act (Wro)
Environmental Management Act (Wm)
Advised distances around industry (2007)
Emission Guidelines on air pollution (2006)
Livestock housing Decree (2008)

## Slide 10: General plan on odour control
Plan enough distance in between
Request always Best Available Techniques
Define maximum Odour Load accepted
Find acceptable situation
    Determine odour strength of source (s)
    Calculate the odour impact in the surroundings
    Decide about the locally allowed situation
Monitor the situation, and ……

## Slide 11: General Plan on odour control
Accepted level
    Nationally advised
    or
    Legally ordered
    Locally decided
Possible role for
    Type of odour
    Type of surroundings
    Other local factors

## Slide 12: Key issues in the History of …
Nuisance surveys
Prototype of maximum odour loads
Dose response inventories /
sectoral approach
Standardisation of means and methods
General policy: local decision needed
    Facilitated by NL / EU rules and regulations on measurements and Best Available Techniques

## Slide 13: Organisation on odour control
Policy
    Local authority (Province or municipality)
    National government (sectoral approach only)
Practice
    Local authority (Province or municipality)
Research and facilitation
    National government (SenterNovem Infomil)
    Research institutes (RIVM, TNO, KEMA, WUR)

## Slide 14: Content
Introduction
Situation in the Netherlands
Our policy and practice in general
Industry : odour control in detail
Agriculture: its regulations and results
Conclusions and recommandations

## Slide 15: Decision needed

## Slide 16: Schedule for systematic determination

## Slide 17: Schedule for systematic determination
Policy
Needed

## Slide 18: Industry and odour nuisance
Define emissions (calculated or measured)
Define abatement techniques
Towards less nuisance with BAT (Alara)
Decision on level of acceptable nuisance
DON’T FORGET the Spatial Planning!!

## Slide 19: Different approaches possible
Guideline for one sector of industry
    Waste water treatment plants
    Breweries
Use of comparable situation elsewhere
Tailor made approach
    For one local situation
    For an industrial area

## Slide 20
Permit Procedure
Odour Nuisance
Top value
Maximum
Orientation value
Target value
Current situation
New situations
ALARA
ALARA

## Slide 21
Example : Agreement for W.T.P.
Odour concentration 98-perc
General
RWZI’S
30
10
3
1
0,3
3
7
Core Existance
Existing V.W.
1
2
New core
New V.W.
EMISSION FACTORS
All different parts like
Surface of Settling Tank
+ Proces related parameters
MEASURES
Normally used
Sometimes useful
Seldom applied

## Slide 22
How do we choose in other cases ?
Odour burden 98 – perc.
30
10
3
1
0,3
?
?
BUSY CITY
INDUSTRIAL SITE
?
?
NATIONAL PARK
QUIET CITY
Good
Possible
Medium
Bad
Very bad
> 40
25 - 40
15 - 25
10 - 15
5 - 10
percentage
Odour nuisance
Environmental
Quality
Standard View on ….

## Slide 23: Content
Introduction
Situation in the Netherlands
Our policy and practice in general
Industry : odour control in detail
Agriculture: regulations and results
Conclusions and recommandations

## Slide 24: Overview of the Legislation
Odour Nuisance and Livestock Farming Act
    In force since January 2007
    List of tolerated systems of production and odour reduction
Immission standards on sensitive objects
Specified Emission factors
Especially made Dispersion Model

## Slide 25: Sources:
Stable:
X-,Y-coordinates:
Point of emission !
Hight of the emission point
Average building hight
Types of stables

## Slide 26
Describing the odour nuisance
Livestock keeping -→ surroundings -→ odour sensitive building
emission (ouE/s) weather conditions odour load
Number of animals type of terrain (ouE/m3 als 98-perc.)
Type of livestock

## Slide 27: Hight of the emission point - effect
ouE/m3 98p

## Slide 28
ouE/m3 as 98-perc.
Area of the low burden
2% of hours per year
odour concentration > 3
Area of medium burden
Area of high burden
*
Visualisation of the odour burden

## Slide 29: Odour concentration limits
Near Houses (ouE/m3, 98-p) | Inside Built-up area | Outside Built-up area
High density Livestock area | 3 | 14
Other area | 2 | 8

## Slide 30: Particular items
Only for animal housing system
Special consideration needed for other sources of odour than the stable itself
Not for all animal categories
are emission factors available

## Slide 31: Attention points
Calculated odour burden
can differ from reality
Prescribed E-factor ≠ measured emissions

## Slide 32: Attention points
Tolerated nuisance levels are nationally determined
Municipalities cannot deny a permit
if complied to immission standards

## Slide 33: Attention Points
Presence of housing areas sets a limit to size of livestock farm
The odour circle sets a limit for development of new housing areas.
Typical Dutch problem?

## Slide 34: Content
Introduction
Situation in the Netherlands
Our policy and practice in general
Industry : odour control in detail
Agriculture: its regulations and results
Conclusions and recommandations

## Slide 35: Conclusions for Dutch Situation
Less nuisance due to Odour Policy
    Unless the Economic Growth
    Severe Nuisance still present
Nuisance level best decided locally
    National standardisation helpfull and necessary
    National legal regulations sometimes needed

## Slide 36: Plans for the future
Quality improvement in measurements and calcultation methods
Quality improvement in policy, law and regulations (keep them up tot date!)

## Slide 37: Future: Equal approach to Noise
Assesment (by RIVM)
of the
quality of environment
In the housing areas
Concentration of odour
( standard )
[ ge/m3, 98-p ]
Noise
( industry )
[ dB(A) ]
Nuisance
( DLO / TLO )
[ % sometimes/often ]
slightly bad
bad
very bad
extremly bad
very good
good
reasonably good
avarage

## Slide 38: Future: Type of area related policy
0,3
1
3
10
30
100

## Slide 39: Recommandations
Standardize methods and means
with quality assurance
Policy, law and regulations
keep them up to date
Organize the right decision
for every local situation

## Slide 40
We wish you Success !